## Slide 1: Testbed System Interface

## Slide 2
Server
(x64-Linux)
Edge1
(aarch64 Linux)
Edge2
(aarch64 Linux)
Edge3
(aarch64 Linux)
XNode
(Coordinator)
Network
(Access Point)
Ethernet
Stereo Camera
Camera
Pixel Display
(16x16) * 10
PWM
USB
XNode
Router 2
XNode
Router 1
XNode
Router 3
XNode
Router 4
XNode
Router 5
Zigbee
Gas Sensor
Gas Breaker
FAN
Light
Eco
FAN
Light
Dust
Curtain
Door
Lock
Light
Touch
Display
HDMI

## Slide 3: Server
휴먼 인터페이스를 위한 터치 스크린, 마이크, 스피커 제공
  터치 스크린: PyQt 기반 UI 출력
  인터넷 연결 시 음성 인식 지원
XNode 코디네이터를 통해 지그비 네트워크 제어
Soda OS 탑재 (Ubuntu 20.04 기반)

## Slide 4: Edge 1 ~ 3
Camera 영상 수집 및 전달
Soda OS 탑재
  1 ~ 2: Ubuntu 18.04 기반
  3: Debian 기반

## Slide 5: XNode Router 1 ~ 5
서버에 연결된 코디네이터를 통해 지그비 네트워크 구성
각각 해당 센서 및 액츄에이터 제어

## Slide 6: Testbed Zigbee Protocols

## Slide 7: Format
Start | Cmd |  | Payload | End
76 | Cmd | Payload Length | Data | 3E

## Slide 8: Server to XNode Send
Cmd | Decsrpition | Payload | Action
01 | Gas Breaker Control | 00 | Off
 |  | 01 | On
02 | Kitchen Fan | 00 | Off
03 | Kitchen Light | 00 | Off
 |  | 01 | On
04 | LivingRoom Fan | 00 | Off
 |  | 01 | On
05 | LivingRoom Light | 00 | Off
 |  | 01 | On
06 | Curtain | 00 | Off
 |  | 01 | On
07 | DoorLock | 00 | Off
 |  | 01 | On
08 | Door Light | 00 | Off
 |  | 01 | On
Cmd | Decsrpition | Payload | Action
01 | Gas Sensor (enable is continue) | 00 | disable
 |  | 01 | enable
12 | Kitchen Sensor (node 1) | 00 | Request
13 | Living Room Sensor (node 3) | 00 | Request
14 | Living Room Sensor (node 4) | 00 | Request
15 | pir Sensor (enable is continue) | 00 | disable
 |  | 01 | enable
16 | Door Sensor (node 5) | 00 | Request

## Slide 9: Server to XNode Recv
Cmd | Decsrpition | Payload |  |  |  | 비고
21 | Gas Sensor | detect : 01, nondetect : 00 |  |  |  | 변화 있는 경우에만 전송
22 | Kitchen Sensor | Temp |  | Humi |  | 
23 | Living Room Sensor | Temp | Humi | Dust_H | Dust_L | Dust = Dust_H <<8 & Dust_L PM 1.0 TSI : 0~1000ug/m^3
24 | Living Room Sensor (light) | Light_H |  | Light_L |  | light = light_H <<8 & light_L PM 1.0 TSI : 0~1000ug/m^3
25 | Pir Sensor | detect : 01 |  |  |  | 변화 있는 경우에만 전송
26 | Door Sensor | Temp |  | Humi |  |